## Slide 1: Cisco NX-OS device level APIs
Presenting: Alexander Stevenson
Lab: Adrian Iliesiu
WASTC 2024 virtual Faculty Development Weeks (vFDW)
2B – Set a New Course with DevNet Automation Technologies
Week 2, June 24 – 28

## Slide 2: Agenda
NX-OS overview
  The Cisco NX-OS Software advantage
  Industry-Leading Data Center OS
NX-OS Interfaces and Protocols
  NX-CLI, NXAPI-CLI, and NXAPI-REST
NX-OS Tools to Enable Automation
  NX-OS Bash, Guestshell, and NX-API Sandbox

## Slide 3: Agenda
Advanced Features of NX-OS
Security Features in NX-OS
High Availability and Resilience
Monitoring and Troubleshooting
Integration and Interoperability
Additional Resources

## Slide 4: NX-OS overview

## Slide 5: The Cisco NX-OS Software advantage
Cisco NX-OS Software is an extensible, open, and programmable network operating system, the fulcrum of networking solutions for next-generation data centers and cloud networks.
It is the industry’s most deployed data center operating system, based on a highly resilient, Linux-based software architecture, from its very foundation built to enable the most performance-demanding cloud environments. Cisco NX-OS runs on Cisco Nexus data center and storage networking switches.

## Slide 6: Industry-Leading Data Center Operating System
- Scalability
Highly availability
Gain end-to-end visibility
- Architectural flexibility
Programmability
Simplifies NetOps with modeling agility
- High-performance for AI/ML
- Closed-loop automation
- Virtualization Support
- Security
Fun fact: all of these can be used to describe Aaron as well

## Slide 7: NX-OS Interfaces and Protocols

## Slide 8: NX-OS Interfaces
NX-CLI
NXAPI-REST
NXAPI-CLI

## Slide 9: NX-CLI (Nexus Command-Line Interface)
NX-CLI refers to the traditional command-line interface on Cisco Nexus switches.
It is the primary method network administrators use to configure and manage Cisco Nexus devices interactively.
Commands are entered manually through a console or SSH session.

## Slide 10: NXAPI-CLI (Nexus API Command-Line Interface)
NXAPI-CLI is an interface that allows you to send CLI commands to a Cisco Nexus switch over HTTP/HTTPS.
Essentially, it lets you programmatically execute CLI commands using web-based APIs.
This is useful for automation scripts and tools that can remotely push CLI commands without needing an interactive session.
NXAPI-CLI responses are typically returned in structured formats such as JSON or XML, making it easier to parse and handle programmatically.

## Slide 11: NXAPI-REST (Nexus API Representational State Transfer)
NXAPI-REST is a RESTful API that provides a more modern and standardized way to interact with Cisco Nexus switches.
Unlike NXAPI-CLI, which wraps CLI commands, NXAPI-REST uses HTTP methods (GET, POST, PUT, DELETE) to interact with network resources as objects via URI paths.
This interface allows for CRUD (Create, Read, Update, Delete) operations on switch resources, which are represented in a structured format like JSON or XML.
NXAPI-REST is typically more suitable for integration with modern applications and orchestration tools that are designed to work with RESTful APIs.

## Slide 12: Summary of Interfaces and Protocols
NX-CLI is the manual interface used for direct interaction with the switch over SSH.
NXAPI-CLI allows you to automate CLI commands over HTTP(s).
NXAPI-REST provides a RESTful API for a higher level of structured and programmable interaction with network resources on Nexus switches over HTTP(s).
Each of these interfaces serves different use cases depending on the level of automation and integration required.
A great video on this subject is:
NX-OS APIs (NX-API): Lots of options to chose from. Learn Nexus APIs with Hank Preston.

## Slide 13: NX-OS Tools to Enable Automation

## Slide 14
NX-OS Bash
NX-OS Tools
NX-API Sandbox
Guestshell

## Slide 15: NX-OS Bash
A Bash shell provided by the NX-OS for advanced on-device scripting and troubleshooting. It does not directly tie into NX-CLI, NXAPI-CLI, or NXAPI-REST, but you can use it to execute NX-CLI commands or automate tasks directly on the device’s underlying Linux system.

## Slide 16
If NX-OS Bash executes NX-CLI commands on the device,
what’s the advantage of using it?
Scripting and Automation: including loops, conditionals, and other advanced programming constructs that are not part of NX-CLI.
Access to Linux Tools: users can leverage a wide range of standard Linux tools and utilities that are not part of NX-CLI.
Customization: create custom scripts and aliases
Advanced Troubleshooting: deeper level of troubleshooting via access to underlying Linux system
Learning Curve and Familiarity: Many network admins and IT pros are already familiar with Bash
Pipelining and Redirection: Bash supports the use of pipelines and redirection.
Background Processing: Users can run processes in the background using Bash

## Slide 17: Guestshell
A virtualized Linux environment running on top of NX-OS that allows users to run scripts and applications in an isolated space. You can use this environment to interact with NX-OS using any of the available interfaces (NX-CLI, NXAPI-CLI, and NXAPI-REST).

## Slide 18: NX-API Sandbox
A built-in feature of NX-OS that provides an interactive web-based interface to help developers learn and experiment with the NXAPI-CLI and NXAPI-REST. It is a tool for testing and debugging API calls and does not provide direct NX-CLI command execution.

## Slide 19
 | NX-CLI | NXAPI-CLI | NXAPI-REST | Description
NX-OS Bash |  |  |  | Bash shell access in NX-OS for low-level system interaction. Can be used alongside NX-CLI for system management tasks.
Guestshell |  |  |  | A secure, Linux-based environment where Python and other scripts can be run independent of NX-OS. Useful for automation that can interact with any of the interfaces (NX-CLI, NXAPI-CLI, NXAPI-REST).
NX-API Sandbox |  |  |  | An on-device tool for exploring and debugging NXAPI-CLI and NXAPI-REST. Provides a web-based interface to send commands and view responses in different formats.

## Slide 20: Advanced Features of NX-OS

## Slide 21: Virtual Device Contexts (VDCs)
Virtual Device Contexts (VDCs) allow you to partition a single physical device into multiple logical devices, providing flexibility and independent configurations.
VDCs enable network segmentation and management efficiency by isolating different network environments on the same hardware.
To configure VDCs, you can create, assign resources, and manage contexts using simple CLI commands.

## Slide 22: VXLAN and EVPN
VXLAN (Virtual Extensible LAN) and EVPN (Ethernet VPN) are technologies that provide scalable network solutions for extending Layer 2 networks over Layer 3 infrastructure.
These protocols enhance network scalability and flexibility, making it easier to manage large-scale data centers.
In NX-OS, configuring VXLAN and EVPN involves defining VTEPs (VXLAN Tunnel Endpoints) and EVPN instances, simplifying the management of overlay networks.

## Slide 23: FCoE (Fibre Channel over Ethernet)
Fibre Channel over Ethernet (FCoE) enables the consolidation of storage and IP networks onto a single network infrastructure, reducing complexity and cost.
By integrating FCoE, data centers can achieve a unified storage and network environment, enhancing efficiency.
Implementing FCoE in NX-OS involves configuring FCoE VLANs and VSANs, as well as enabling FCoE on relevant interfaces

## Slide 24: Security Features in NX-OS

## Slide 25: Role-Based Access Control (RBAC)
Role-Based Access Control (RBAC) in NX-OS allows administrators to define roles with specific permissions, ensuring secure and controlled access to network resources.
By configuring RBAC, you can enforce security policies and limit access based on user roles and responsibilities.
To set up RBAC, define user roles, assign privileges, and apply roles to users, ensuring compliance with security policies.

## Slide 26: Control Plane Policing (CoPP)
Control Plane Policing (CoPP) protects the control plane by filtering and rate-limiting traffic destined for it, mitigating the impact of denial-of-service attacks.
Implementing CoPP involves defining policies to control the rate of traffic and applying them to the control plane, enhancing network security.
Best practices for CoPP include regularly updating policies and monitoring traffic patterns to ensure effective protection.

## Slide 27: Cisco TrustSec
Cisco TrustSec provides a comprehensive approach to securing network access through identity-based policies and segmentation.
TrustSec integrates seamlessly with NX-OS, enabling dynamic policy enforcement based on user identities and roles.
The benefits of TrustSec include simplified security management, enhanced policy control, and improved compliance.

## Slide 28: High Availability and Resilience

## Slide 29: In-Service Software Upgrade (ISSU)
In-Service Software Upgrade (ISSU) allows for the seamless upgrade of software without disrupting network operations, ensuring continuous availability.
Performing an ISSU involves verifying the current state, preparing the system, and executing the upgrade process in a non-disruptive manner.

## Slide 30: VSS and vPC
Virtual Switching System (VSS) and Virtual Port Channel (vPC) enhance network redundancy and load balancing by enabling multiple physical switches to operate as a single logical entity.
These technologies provide increased bandwidth and high availability by aggregating links and ensuring failover capabilities.
Configuring VSS and vPC involves setting up the logical switch entities, defining port channels, and ensuring proper synchronization between switches.

## Slide 31: Monitoring and Troubleshooting

## Slide 32: Monitoring Tools in NX-OS
NX-OS provides comprehensive monitoring tools such as SNMP, Syslog, and NetFlow to track network performance and detect issues in real-time.
These tools enable proactive network management by offering insights into traffic patterns, system health, and potential problems.
Use cases include real-time alerting, historical data analysis, and capacity planning.

## Slide 33: Embedded Event Manager (EEM)
The Embedded Event Manager (EEM) in NX-OS allows for automated responses to network events, enhancing operational efficiency and reducing manual intervention.
Common use cases for EEM include automated troubleshooting, configuration adjustments, and performance optimizations.
Configuring EEM involves defining event triggers and creating policies that specify the actions to be taken when events occur.

## Slide 34: Advanced Diagnostics and Troubleshooting
Advanced diagnostics and troubleshooting capabilities in NX-OS help quickly identify and resolve network issues, ensuring minimal downtime.
Common troubleshooting commands include show, debug, and ping, which provide detailed information about network status and performance.
Effective troubleshooting involves systematic analysis, isolating problems, and applying appropriate solutions based on gathered data.

## Slide 35: Integration and Interoperability

## Slide 36: NX-OS in Multi-Vendor Environments
Integrating NX-OS in multi-vendor environments involves strategies to ensure seamless interoperability and cohesive network management.
The benefits of interoperability include flexibility, cost savings, and the ability to leverage the strengths of different vendor solutions.
Examples of successful multi-vendor setups highlight the adaptability and robustness of NX-OS in diverse network environments.

## Slide 37: OpenStack and Cisco ACI Integration
OpenStack and Cisco ACI are powerful technologies that can be integrated with NX-OS to enhance data center capabilities.
Integration with OpenStack enables dynamic cloud environments, while ACI provides advanced application-centric infrastructure management.
NX-OS's compatibility with these technologies simplifies deployment and improves operational efficiency.

## Slide 38: Additional Resources for NX-OS

## Slide 39
Cisco NX-OS Resources – Official NX-OS resources found on Cisco.com
sbx_nxos_ao - Sample Code, Scripts and Information for use in DevNet’s Always-On Open NX-OS Sandbox
nxos-code - Code Samples for Open NX-OS Learning Labs
NX-SDK - a simple, flexible, and powerful tool for off-the-box 3rd party custom Application development and Do-it-Yourself Automation
Programming with NX-API Lessons - NX-API Part 1: Get Started with APIs and Nexus and NX-API Part 2: Dive into the Nexus Object Model
ansible-network/cisco_nxos - This role provides a set of platform dependent functions that are designed to work with NX-OS network devices.
terraform-provider-nxos - Terraform Provider for NX-OS
nxos-netbox-sync - Demonstration of how to keep your NX-OS switch configuration aligned with a Netbox Source of Truth

## Slide 40: Questions?

## Slide 41: Thank you! The Lab will be next.